## Slide 1: LABA: Design analysis
110061519 楊博舜

## Slide 2: Outline
Briefly introduction to the algorithm or overall system
Explain the original code/system/pragmas and how you implement it
Examine the synthesis log to list what steps the tool takes during synthesis
Analyze the timing/performance/utilization
If possible, share how you optimize the design and the trade-off you make
Explain what you observed and learned

## Slide 3: Briefly Introduction to the Algorithm or Overall System

## Slide 4: Briefly introduction to the algorithm or overall system
In this tutorial, we are going to learn how to use Vitis HLS to build, analyze, and optimize a hardware kernel. There are a few ways to do it, such as pipelining, using dual-port RAMs, array partitioning, and dataflow optimization.
The algorithm implemented in hardware is discreate cosine transform, DCT. It can process data into frequency domain, similar to Fourier transform. What makes them different is that DCT only uses real numbers. DCT is often used to process signals and images. Assume that we have a matrix with size N×N, and the values are denoted by f(x,y). The formula is shown below.

## Slide 5: Explain the Original Code/System/Pragmas and How You Implement It

## Slide 6: Explain the Original Code/System/Pragmas and How You Implement It
This is the top function. It is obvious that the kernel will read data, process the data, and then write the data. Note that DCT_SIZE is specified as 8 in the design.

## Slide 7: Explain the Original Code/System/Pragmas and How You Implement It
This is the function that reads data. We can see that it reads a 1d array into a 2d array.

## Slide 8: Explain the Original Code/System/Pragmas and How You Implement It
This is the function that writes data. We can see that it writes a 2d array into a 1d array.

## Slide 9: Explain the Original Code/System/Pragmas and How You Implement It
This is the core function of DCT algorithm. The function is further divided into 4 parts, processing row, transposing, processing column, and transposing again. In this way, they can reuse the same function.

## Slide 10: Explain the Original Code/System/Pragmas and How You Implement It
Here, I will show how they divide the formula into row and column steps with N=8.
We can see that the formula has the similar operation for sum over x and sum over y. They declare another function to do the operation row by row, and transpose is required.

## Slide 11: Explain the Original Code/System/Pragmas and How You Implement It
In this function, they input a row, and calculate the accumulated sum (inner loop) for each element (outer loop). Here, a 8×8 coefficient table, dct_coeff_table.txt, is used.
In general, people convert floating numbers into integers before computing in hardware. Here, they implement the conversion by multiplying the floating numbers by . Therefore, the coefficients can be calculated in this way.

## Slide 12: Examine the Synthesis Log to List What Steps the Tool Takes During Synthesis

## Slide 13
Project and solution initialization loads source and constraints files, and configures the active solution for synthesis.
Start compilation reads source files into memory.
Interface detection and setup reviews and generates port and block interfaces for the function.
Burst read and write analysis for ports/interfaces.

## Slide 14
Compiler transforms code to operations.
Performs Synthesizeability checks.
Automatic pipelining of loops at tripcount threshold.

## Slide 15
Unrolling loops, both automatic and user-directed.
Array partitioning.
Balance expressions using associative and commutative properties.
Loop flattening to reduce loop hierarchy.

## Slide 16
Partial write detection (writing part of a memory word)
Finish architecture synthesis, start scheduling.
End scheduling, generate RTL code.

## Slide 17: Analyze the Timing/Performance/Utilization

## Slide 18: Performance Profile
This is the latency/loop table resulting from the original setting in the tutorial. To see how it calculate the latency of loops, I disable the pipeline of RD_Loop_Row. The result is shown in the next page.

## Slide 19: Performance Profile
We can see that if a loop is pipelined, the latency is small. The value is approximately Iteration Latency+Interval×(Trip Count-1)=10. If a loop is not pipelined, the latency is large. The value is Iteration Latency×Trip Count=104.
From the latency table, we can also see that the critical blocks to optimize are the dct_Pipeline_Row_DCT_Loop_DCT_Outer_Loop and dct_Pipeline_Col_DCT_Loop_DCT_Outer_Loop, since their latency are largest. This can also be seen on Function Call Graph Viewer by setting heat map.

## Slide 20: Function Call Graph Viewer

## Slide 21: Schedule Viewer
From the viewer of the top module, we can find those modules introduced above, and they are arranged in order. We can also see some blue lines representing the data dependencies.

## Slide 22: Schedule Viewer
From the module hierarchy, we can select the modules and loops to view their schedule. Besides, we can also right click on the operation to see where it was called.

## Slide 23: Schedule Viewer
From the properties, we can also see the latency of selected operation.

## Slide 24: If Possible, Share How You Optimize the Design and the Trade-off You Make

## Slide 25: Configure the Pipeline Loops Threshold
In this method, we are asked to modify pipeline_loops as 6. It enables loops with an iteration count below 6 to be pipelined automatically.

## Slide 26: Configure the Pipeline Loops Threshold
After synthesis, we can see that the latency increases a lot, and that many loops are not pipelined, resulting to large latency. By the way, increasing the value does not help in this case, since there is no loop with iteration counter larger than the default value, 64.

## Slide 27: Configure the Pipeline Initiation Interval
In the tutorial, we are asked to modify the II of dct_2d as 4.
After synthesis, although the overall latency is decreased, there is timing violation.

## Slide 28: Configure the Pipeline Initiation Interval
We can see that the timing violation occurred during reading data. I tried to figure out how to fix it by adding some directives, but end up failing.

## Slide 29: Configure the Pipeline Initiation Interval
I tried to modify the II as 2, and it works well. The figure above is the result performance. We can see that the latency is greatly decreased.

## Slide 30: Assign Dual-port RAMs with BIND_STORAGE
In the tutorial, we are asked to use BRAMs to store col_inbuf and buf_2d_out. After synthesis, the result is shown in the figure below.
We can see that the total latency increases a lot. Besides, II violation is issued (II violation does not influence the co-simulation result. In HLS, II violation will be issued if II is not 1.)

## Slide 31: Assign Dual-port RAMs with BIND_STORAGE
Take a look at the report, and we can see that it uses more resource as well. Therefore, I think that this method is not for this application.
Original method | This optimization method

## Slide 32: Assign Dual-port RAMs with BIND_STORAGE
I also tried to remove the II violation. I think that violation happened since the bandwidth of BRAM is not large enough. Therefore, I try to partition the array (the next optimization method). The result is shown below.
We can see that the latency is reduced (664 -> 475), but still larger than that of the original method (444). To remove the II violation of writing output, I enlarge the II of WR_Loop_ROW as 2. The result is shown in the next page.

## Slide 33: Assign Dual-port RAMs with BIND_STORAGE
No II violation is issued, and the latency decreases a little (still larger than that of the original method).

## Slide 34: Assign Dual-port RAMs with BIND_STORAGE
Again, compare their utilization, and we can see that the original method looks better.
Original method | This optimization method

## Slide 35: Assign an Array Partition
In the tutorial, we are asked to partition the arrays, col_inbuf and buf_2d_out. The result is shown in the figures below.
We can see that the iteration latency of WR_Loop_Row decreases. However, I have no idea why the overall latency increases.

## Slide 36: Dataflow Optimization
In the tutorial, we are asked to add pragma DATAFLOW to the directives. This pragma enables task-level pipelining. The HLS tool will analyze the dataflow between functions and see whether they can overlap or not. The comparison result is shown in the figure below.

## Slide 37: Dataflow Optimization
After running co-simulation, we can see the dataflow graph. From the graph, we can see that the three blocks, dct_2d, read_data, write_data are not running in parallel.

## Slide 38: Dataflow Optimization
From the process table below, we can see some information.

## Slide 39: Dataflow Optimization
From the channel table below, we can see the channel type and the bit width.

## Slide 40: Dataflow Optimization
Can it be further optimized? I tried the pipeline method taught in second method, and removed the array partitioning. The result is shown in the figure.
We can see that the interval is now only 84.

## Slide 41: Explain What You Observed and Learned

## Slide 42: Explain What You Observed and Learned
In this lab, I learned some tools to help us analysis our design, such as schedule viewer, function call graph, and dataflow viewer. I also learned some optimization methods, such as pipelining, using dual-port RAMs, array partitioning, and dataflow optimization.

## Slide 43: END